## Slide 1
FlashPoint
Lightning strike localization & wildfire ignition watch on the Sage Grande Testbed
Cameras catch the flash. Microphones catch the thunder. Weather decides when to listen.
Sage Summer Camp 2026 hackathon proposal · Samuel Watson · every number in this deck verified against the live fleet, July 21 2026
Notes: FlashPoint: turn the existing Sage fleet into a lightning localization and wildfire ignition-watch system. Every claim in this deck was verified live against the fleet on July 21, 2026.

## Slide 2
THE PROBLEM
Lightning fires start silently, in country nobody watches
In the remote mountain West, lightning-ignited fires account for the majority of area burned — and they start far from roads, stations, and eyes.
Holdover fires smolder for days before flaring — the strike is the earliest possible warning, and today nobody connects strikes to a follow-up watch.
Commercial lightning networks map strikes, then stop — no local fuel context, no camera follow-up, no ignition watch, and nothing at the network's edge.
The window that matters is strike → smolder → flame. FlashPoint lives inside that window.
days
a holdover fire can smolder after the strike — the watch window
10–15 km
distance thunder is audible — one node covers a whole drainage
$0
new hardware needed — mics, cameras & weather sensors are already deployed
Notes: Lightning fires begin in remote country; holdover fires give a multi-day warning window that no current system uses. Commercial networks locate strikes but do not watch for ignition.

## Slide 3
THE IDEA
From storm forecast to responder alert — one edge pipeline
1
ARM
forecast & local sensors switch nodes to storm mode
2
FLASH
sky cameras timestamp the flash — a free absolute clock
3
THUNDER
mics time the rumble; Δt × 343 m/s = range, per node
4
LOCALIZE
ranges from several nodes triangulate the strike
5
WATCH 72 h
PTZ & smoke detectors re-aim at strike bearings
6
NOTIFY
ignition-risk card to responders, human-reviewed
Raw video and audio never leave the node — only strike events, a few hundred bytes each. That is the edge-AI core of the design.
Every localized strike becomes a 72-hour wildfire ignition watchpoint.
Notes: Six stages: arm on weather, timestamp flash optically, time thunder acoustically, per-node range, multi-node fix, then a 72-hour ignition watch with responder notification. Only tiny event records leave the node.

## Slide 4
FEASIBILITY · PHYSICS
The flash is a free clock — no network sync needed
Light arrives instantly
Every node sees the same flash at effectively the same moment — a shared time-zero, delivered by nature.
Each node self-clocks flash-to-bang
One clock per node measures Δt to its own thunder onset. Range = Δt × 343 m/s. Cross-node clock sync — the hardest problem in acoustic localization — is simply not required.
Ranges triangulate
Three self-clocked ranges give a stable trilateration fix — far better conditioned than timing-difference methods.
Thunder carries
Audible 10–15 km: nodes tens of km apart co-detect the same strike (a gunshot carries only 1–2 km).
0 ms
cross-node clock synchronization required in flash-anchored mode
±150 ms thunder-onset error → ±51 m of range
Honest asymmetry: flash detection is easy at night, weak at midday — daytime falls back to thunder-only timing across nodes (simulated next slide). Nocturnal dry-lightning storms are a real ignition scenario.
Notes: Key physics: the flash gives all nodes a shared time-zero, so each node independently measures range with its own clock. This removes the cross-node synchronization problem entirely in flash mode. Daytime falls back to thunder TDOA.

## Slide 5
FEASIBILITY · THE FLEET IS ALREADY BUILT
The fleet is already deployed — verified census
51 + 51
Chicagoland — the lab
51 mic + 51 camera nodes across 32 × 49 km: one connected thunder array. Peak July storm season for live validation.
2×
Lakeview, MT — the flagship
Twin co-located mic+cam nodes (W084 + W06F) in sagebrush ignition country, recording continuously since 2023.
4+
Fire-country sentinels
Palomar Mtn CA · Selma OR (Siskiyou) · Moran WY (Teton) · Lubbock TX — single nodes giving range + bearing per strike.
2
Salt Lake City pair
W045 + W029, ~4–5 km apart: monsoon lightning meets Wasatch-front WUI.
3
Hawaii — same controller, wind trigger
Lahaina node has thermal + PTZ. HI lightning is rare, so storm-mode arms on red-flag wind events instead — the architecture generalizes.
0 mics
Colorado — the gap we found
6 nodes in prime lightning country, zero microphones. A concrete hardware recommendation for the Sage team.
Source: Sage node manifests + live data API, queried July 21 2026.
Notes: Census verified from the live manifest: Chicagoland has a full 51-node array; Montana twins in fire country recording since 2023; single sentinels across the West; Colorado is a capability gap worth reporting.

## Slide 6
FEASIBILITY · SIMULATION ON REAL COORDINATES
Block-level accuracy from a Monte Carlo on the real network
Thunder-timing mode (the harder, daytime case) simulated over the actual GPS positions of Chicagoland's 51 microphone nodes — 250 random strikes per setting, ≥3 detecting nodes within 12 km.
Chart: Median strike-location error (meters)
| 50 ms onset error | 100 ms (realistic) | 200 ms onset error
Median strike-location error (m) | 135 | 216 | 331
~216 m median at realistic timing error
Competitive with community lightning networks (km-class); enough to say which drainage to patrol.
Fringe fixes are gated, not trusted
Outside the array core, geometry degrades — every fix ships with an uncertainty ellipse and a quality gate.
Flash mode is even better
Absolute per-node ranges (no sync) stabilize the solver — the deep reason to fuse cameras with microphones.
Context: the same method, tighter array
On Argonne's 16-node campus cluster, sibling sims hit 16–22 m median for impulsive sounds.
Notes: Monte Carlo on real node coordinates: 135-331 m median error depending on thunder onset precision. Fringe geometries are quality-gated. Flash-anchored mode is more stable still.

## Slide 7
PRELIMINARY RESULTS · WE RAN IT — AND LET SATELLITES GRADE IT
Two satellites falsified our first result — then found the real storm
Retrospective on the Kitten Fire (Grand Teton, discovered 02:04 UT Jul 3 2025, ~12 km from node W06C): 518 archived audio clips analyzed, then cross-validated against GOES-18 AND GOES-19 GLM lightning data.
★ THE AUDIT — audio alone, falsified
A v0 acoustic classifier (low-band transients + anemometer wind veto) proposed thunder candidates. We let two independent satellite lightning mappers grade every one:
17
confident 'thunder' detections from 518 archived clips
0 / 17
survived GLM review — no flash within 50 km, either satellite, any event
Lesson
single-modality detection false-alarms with total confidence. Fusion isn't a feature — it's the design.
Falsification is a feature: the pipeline catches its own plausible-but-wrong answers.
★ THE REAL STORM — found via GLM
Scanning satellite lightning around the fire point located the actual ignition storm — and satellite-anchored re-listening recovered what audio-only had missed:
219
GLM flashes ≤25 km, 22:00–00:00 UT Jul 2 — closest 3.1 km from the fire point; discovery 3 h later
22
flash→bang arrivals landing inside archived clips — thunder recovered, buried in the rain noise that blinded audio-only
Wall.
during the ignition storm, the node's PTZ camera was pointed at a cabin wall — storm-mode camera control exists for exactly this
Preliminary results, not promises — the pipeline already ran end-to-end.
Also verified: the Selma bust — 14 natural-cause fires in one day (Jul 8 2025) near W067; node gauge 0.05 mm all week; SMAP soil moisture 0.084. Sources: Sage data API, NIFC WFIGS, GOES-18/19 GLM (AWS open data), NASA SMAP/POWER.
Notes: The strongest evidence: real lightning fires occurred within earshot of recording nodes. The Kitten Fire was 6 km from a node capturing audio every 5.5 minutes; the Selma bust gives imagery and the dry-lightning test. These archives exist today.

## Slide 8
THE REQUESTED FEATURE · WEATHER-CONDITIONED SENSING
Storm mode: always-on sensing when weather says so
0
OUTLOOK — pre-arm
Daily NWS / SPC convective & fire-weather outlooks (free API). Nodes in the risk area load storm profiles and wait.
1
APPROACH — arm
The node's own sensors see the pressure fall and wind shift; lightning-network cells within ~100 km confirm. Snapshot samplers are swapped for continuous ring-buffer audio + video via Sage's job API.
2
STORM — full capture
First flash or thunder locks storm mode: continuous capture, real-time strike mapping, live map — for the storm's duration plus 30 min.
3
AFTERMATH — 72 h holdover watch
Sensors revert to save power & storage. PTZ cameras physically re-aim along each logged strike bearing; smoke detection gets GPU priority; a vision model reviews strike sectors daily.
Guardrails: storage, thermal & shared-GPU budgets · hard caps on continuous hours · auto-revert on timeout · every mode change audit-logged with its trigger. Sensing effort is spent exactly where information lives — the token-economy idea, applied to physics.
Notes: The storm-mode controller: pre-arm on forecast, arm on local sensors and approaching cells, full continuous capture during the storm, then a 72-hour holdover watch in which PTZ cameras physically re-aim along strike bearings and smoke detection gets priority. Guardrails and audit logging throughout.

## Slide 9
FROM STRIKE TO RESPONDER
Every strike is scored for ignition risk — then a human decides
Strike localized
position + uncertainty ellipse from the fusion engine
Dry-lightning flag
the node's own rain gauge: strike with < 2.5 mm rain = the dangerous kind
Fuel dryness
days-since-rain locally + public fire-danger indices
Notification card
map, time, risk score, follow-up smoke-check schedule — to a human review queue
Built for aid-routing, engineered for trust
Human review before anything is dispatched — no automated response. · Published error bars on every fix — no accuracy theater. · Raw audio/video processed and discarded on-node; only events leave. · Full audit log of every alert and its disposition.
Notes: The wildfire loop: localized strike, dry-lightning flag from the node's own rain gauge, fuel dryness context, then a human-reviewed notification card. Responsible-use design is built in from the start.

## Slide 10
WHY THIS MUST LIVE AT THE EDGE
Edge AI isn't a feature here — it's the load-bearing wall
Detection runs on the node
An always-on DSP gate (CPU) triggers a spectrogram classifier (GPU) in tens of milliseconds — flash and thunder are found where the sensors are.
> 10,000× data reduction
Continuous audio ≈ 8 MB/min/node; a strike event is ~300 bytes. Events, not streams, cross the backhaul — that's what makes 100+ remote nodes affordable.
Works when the network doesn't
Remote fire country loses backhaul first. An edge node keeps sensing, localizing, and logging through the outage — and syncs when the link returns.
Local models first, big models rarely
On-Thor models draft incident cards and screen events; a frontier model is consulted only for the ambiguous few — the camp's token-economy philosophy, in production form.
Privacy is structural, not procedural: microphones in public space never ship audio — only "thunder, 14:32:07.412, confidence 0.93."
Notes: Edge computing rationale: on-node inference, four-orders-of-magnitude data reduction, disaster resilience when backhaul fails, and local-first model usage.

## Slide 11
VALIDATION & DEMO INSURANCE
Ground truth is free — the demo survives blue skies
Independent ground truth
Blitzortung community lightning network — free live + historical strike feed to score every fix against
NOAA GOES GLM satellite lightning mapper — independent detection recall check from orbit
The node's own weather station — dry vs. wet lightning, per strike, on the spot
Target: match strikes to Blitzortung/GLM, report error CDF in-core vs. fringe, and quantify what storm mode captured that snapshot cadence would have missed — the number that justifies the whole idea.
No storm during demo week?
Replay harness
Historical Blitzortung storm streams + synthetic onsets drive the full pipeline end-to-end — live map, alerts, everything — without weather.
Bench rig
A photo strobe + speaker playing thunder at measured distances validates flash-to-bang ranging in a parking lot.
And the odds are decent anyway
Chicago in late July averages a thunderstorm every few days — the lab array sits under one of the stormiest weeks on the calendar.
Notes: Validation against Blitzortung and the GOES satellite mapper is free. Demo insurance: a replay harness and a strobe/speaker bench rig mean the pipeline demos even without a storm.

## Slide 12
ONE HACKATHON WEEK
Six days from zero to live strike map
1
Flash + thunder detectors on ring-buffer frames & audio (shares EchoGuard's onset stack)
2
Per-node flash-to-bang range engine + flash↔thunder pairing by azimuth
3
Storm-mode controller wired to NWS outlooks, approach triggers & the Sage job API
4
Multi-node fusion with quality gating + live strike map
5
72-h holdover watch: PTZ re-aim + smoke priority; responder notification cards
6
Metrics freeze · Kitten Fire retrospective · poster & 5-min demo
Camp deliverables, covered
ECR apps: flash/thunder detector + the storm-mode controller (reusable far beyond lightning) hermes-profile/: trigger policies + notification tools for the shared Sage agent Writeup: sim + census + archive case studies = a verified-feasibility spine Poster: error map, storm-mode capture gain, Kitten Fire timeline Team: 4 roles — DSP/edge · controller/agent · fusion/geometry · validation/demo
Notes: Six-day build sharing 70% of its stack with the EchoGuard sibling project, mapped directly onto every required camp deliverable.

## Slide 13
The fleet is built. The physics is free.
The archive already holds the proof.
0 / 17
audio-only detections that survived dual-satellite review
3.1 km
closest GLM flash to the fire point — 3 h before discovery
22
flash-to-bang arrivals recovered inside archived clips
Next: build the storm-mode controller + flash/RF/audio fusion with the camp team — the retrospective proved why every leg is necessary.
FlashPoint · Sage Summer Camp 2026 · Samuel Watson · sources: Sage manifests & data API, NIFC WFIGS, NWS, Blitzortung, GOES GLM — all queried live July 21 2026
Notes: Close: the infrastructure exists, the physics removes the hardest engineering problem, and a real lightning fire already happened next to a recording node. Next step is the retrospective analysis, then the build.